## Slide 1: Innovative decisions

## Slide 2: VOIP COMPONENT
VoIP is a communication technology that enables voice calls to be transmitted over IP-based networks like the Internet.

## Slide 4: Five Major VoIP Network Components
MCUs
IP Network
Call Control
Voice and Media Gateways
User End Devices

## Slide 5
Call Control is the brain of a VoIP system. It manages call setup, call ending, and signaling. It can be software, hardware, or a soft switch. It is easy to manage and secure compared to other components. In hosted VoIP systems, provider security should be reviewed.
Call Control:

## Slide 6
Voice and Media Gateways:
The voice or media gateway connects the VoIP network to external networks such as the Public Switched Telephone Network (PSTN).
Connect VoIP networks to the PSTN Convert voice between TDM and IP formats The media gateway transports voice traffic over the IP network. Enable external call termination and media handling

## Slide 7: Voice is broken into packets Packets are transmitted using RTP (Real-Time Transport Protocol) over UDP Voice traffic needs priority over data traffic QoS (Quality of Service) ensures clear voice calls IP Network This is the network that carries voice and signaling data. Voice Transmission:

## Slide 8
Used for audio and video conferencing Also called conference bridges Connect multiple users in one session Can be hosted internally or externally Security is critical because one failure affects many users Must secure all connected media types
MCU (Multipoint Control Unit):

## Slide 9: User End Devices These are the devices used by users to make or receive calls. Use TCP/IP protocol Get IP address using DHCP Communicate with the call processing server
User End Devices:
Types of End Devices:
VoIP Phones: Hardware phones that connect to IP network Softphones: Software-based phones on laptops or PCs Consoles: Special-purpose systems used in controlled environments